## Slide 1: Fixed BNG PGW on GO over NFF
High Level Design
AT&T & Intel

## Slide 2
RG
UE
Radio
SAE-GW
BNG
LAN
Wired GE no VLAN other than .1p
LTE or NR
MME
HSS
RADIUS
LDAP
GTP-C
GTP-U
Default bearer for RG IP traffic
TEID <-> subscriber binding
IMSI + other subscriber info

## Slide 3
RG
UE
NodeB
SAE-GW
BNG
LAN
MME
HSS
GTP-C
GTP-U
NAS signaling
DNS
Authentication (IMSI, …)
Create Session (PAA, PCO)
S/P GW resolution
UE brings up bearer
APN request
Location update (IMSI, …)
NAS
Modify bearer (TEID)
Attach accept/complete (PAA, PCO)
Default Bearer Active
SLAAC ICMPv6 RA (/64) or in PAA??
TEID <-> Subscriber binding
RADIUS auth use IMSI as key
RADIUS
A.1 -> GTP session TEID 11
C/60 ->

## Slide 4
RG
UE/OWA
eNodeB
SAE-GW
BNG
LAN
Wired GE no VLAN other than .1p
LTE or NR
MME
HSS
RADIUS
LDAP
S11
GTP-C
S1U GTP-U
802.1x
802.1x EAP RADIUS proxy
RADIUS
DHCP, DHCPv6 IA_NA, IA_PD
DHCP/DHCPv6 relay
Network management
CMS/Other OAM
New – UE manager
Uses cached info from GTP-C triggered RADIUS
Time
After UE PDN is up
Note that the RG will be trying 802.1x before UE PDN is up. But UE will not respond until after PDN is up.
DHCP
SGi

## Slide 5
3
2
1
RG
UE
NodeB
S11 Adaptor
LAN
MME
HSS
RADIUS
S1-MME
GTP-U
S11|GTPV2C
UE FTEID Hash
UE IMSI Hash
Select/Update engine
S11 Event Reflector Tbl
Query/Update engine
UE Context DB
bng_sla_hash
Select/Update engine
AVP Event Reflector Tbl
Query/Update engine
Flow Rule DB
S6a
GTP-U TEID Match
UE Context
SDF Filters (LPM)
ACL Profile filters
QoS Profile Filters
TM (Shaper)
S1U
SGi
UE/TEID Cache
sla_profile_hash
Query/Update client
BNG-PGW NFF
Data Path (DP)
App.
Servers
BNG-PGW on GO | NFF Design
Preliminary Requirement/Feature set: Phase 1 Q1’18:
UE+NodeB, MME, HSS ng4T emulation
IPv4 on all interfaces (S1-MME, S11, S1U, SGi).
#of UEs/Flows = 10K; 1 MPPS
QoS/TM Shaper Phase 2 ~Q2’18
ARP on S1U/SGi. ICMP Phase 2 ~Q2’18
IPv6 Phase 2 Q2’18 target
BNG-PGW NFF
Control Plane (CP)
bng_sla_hash
imsi_profile_grp[]
sla_profile_db
imsi_DB-LDAP
sla_DB-LDAP
AT&T OSS,BSS
ZMQ: PUB|SUB
Phase 1 Q1’18 stages:
#1: Areg + Ashok
#2: Ashok + ng4T
#3: Ashok + ng4T + Areg

## Slide 6: BNG Forwarded Architecture Model – high level
YANFF BNG
      In user space
      Owns SR-IOV S1U and SGi interfaces
        Hides subscriber GTP-U interface data
        OS does not see the subscriber address space/routes
        ICMP, ICMPv6 (RA, RS, ND), DHCP, DHCPv6 has to be handled by YANFF modules
      Provides logical vETH interface to OS
      Keep S11 as a separate physical interface from SGi and S1-U
      Initially prefer SGi and S1-U be separate

## Slide 7: Requirements (* = Not Day One)
Subscriber = GTP-U TEID session (no MDU/multisubscriber); IMSI is identifier
Subscriber “context” – all traffic to/from GTP session [eventually, would like to support dedicated bearers in same PDP session]
Will only do the minimal requirements for S1-U and S-11 necessary for fixed wireless
e.g., for S1-U, will not support GTP sequence numbers, or extension headers
ACL filtering, classification and marking
IPv6 transport (e.g., for GTP)
ipv4v6 bearer type
Traffic manager – per subscriber shaper *?
Counters (byte, packet) by subscriber+class
DHCP, DCHPv6 – for RG support (not UE addressing bearer addressing)
single host model per subscriber context, i.e., a new host (MAC) replaces lease of previous host; single NA and PD per sub
icmp/icmp6 error and application handling (RA, RS, ND)
RADIUS – for subscriber policy and networks behind UE
BGP – for advertising pools on SGi to PDN
* MTU check with fragmentation/reassembly
* Failure/reboot recovery – preserve GTP-C info? How is reset done in GTP-C?
* Subscriber service info – persistent (survive restart?), redundant?
*yang model for base config (pools, RADIUS, BGP, interfaces, ACL and QoS policies, logging)
*Subscriber mirroring (lawful intercept)
*Combine/share physical interface supporting logical VFs for S1u, SGi and S11
*GTP echo?

## Slide 8: IP applications on subscriber interfaces
These applications need to be in the BNG forwarding engine for the S1-U interface
Very low rate (although need DOS/abuse protection rate limiter)
Subscriber interfaces here = PDP context
  IPv6: RA, RS and ND processing
  ping (icmp echo) - also need hook to inject and return response to management plane
  icmp error processing (TTL, packet too big)
  packet capture/mirroring (e.g, for operations or lawful intercept)
  DHCP/DHCPv6 (this is for networks behind UE, not the UE PDN session addresses)
Also need icmp and ARP processing for SGi interface in the BNG

## Slide 9: Miscellaneous notes/comments
Networks behind UE model:
  Why does this require so many networks? UE IPv4, RG WAN IPv4, UE IPv6 /64, RG WAN IPv6 /64, RG LAN IPv6 PD (/60); Plus an optional static IPv4 LAN subnet.
      For broadband service we now have networks behind the mobile UE and not just a single UE host. The mobile hotspot approach is very limiting and would have problems supporting some home network setups and business broadband network setups.
      Alternatively: do a passthrough type model with one route for IPv4 and one for IPv6
        UE gets public IPv4 and passes through to RG WAN. UE intercepts certain IPv4 traffic for its own purposes (assuming not running a separate management APN on UE)
        For IPv6 use a /59 – first /64 goes to UE, second /64 goes to RG WAN, second /60 goes to RG LAN PD. UE does DHCPv6 for a PD and gets the /59 with the Prefix Exclude Option covering the UE /64
      However, our target model for broadband is to keep user Internet traffic addressing separate from internal management.
        The RG WAN IPv4 is Internet routeable and used for the customers home traffic and for management. We have to use difficult to manage whitelists for RG management.
        Would prefer that the UE IPv4 management not use the same address as the RG and then also have to implement whitelist management.
        For IPv6 subscriber Internet traffic uses the /60 on the LAN and comes from an Internet reachable address space. The RG WAN IPv6 comes from a different address space that is not routed to the Internet, but only routed inside AT&T networks. Again, don’t want the UE address space to be combined with RG LAN.
        Could save one network by using a /63 to create the UE bearer /64 and RG WAN /64 or could try passing through the UE /64 for the RG WAN. But would still the RG LAN /60 PD.
        If we have 10,000 subs and 5 routes each then that is 50,000 routes. That should not be a problem for a longest prefix match FIB, when compared to the internet route table that has ~700,000 routes inside AT&T backbone

## Slide 10: Notes/Comments Continued
For fixed wireless broadband, the intent is to assign apriori the subscriber to a specific BNG based on a capacity management model implemented at order initiation and store this in the HSS
  This allows the subscriber to retain the same address space
  FW broadband is always on. No mobility, no need to go IDLE and save power
  Subscriber ordered speed is known and fixed.
  We have very good models for bandwidth usage when aggregating large numbers of subscribers on a BNG
  But we reserve the right to groom subscribers if profiles or capacity management models change
There is almost no signaling load for MME and the BNG
  Only on initial turnup or on reboot (a brownout/blackout recovery would be highest signaling load – these UEs will not have a batter like mobile UEs)
There is no NAT or firewall or proxy (MSP) for the SGi traffic for fixed broadband. Broadband networks services support the end-to-end principle as much as possible. Inbound initiated TCP/IP connections are allowed. Perimeter security is provided on premise by the RG.
We may consider a separate APN connection for UE management. I would want to require that subscriber user plane on the UE be in a Linux network namespace to isolate it from UE management.
Currently there is no interest in supporting VoLTE at AT&T on NGFW or 5G FW. Voip will be inband on the RG as done today on AT&T wired broadband. But this would ideally use dedicated non-GBR bearers on the same Internet APN UE connection.